## Slide 1: ANALOG DESIGN INTERNSHIP
INTERN NAME - AFZAL MALIK
College/UNIVERSITY – ZAKIR HUSAIN COLLEGE OF ENGG. & TECH.
ALIGARH MUSLIM UNIVERSITY
COURSE- BACHELOR OF TECHNOLOGY (ELECTRONICS ENGG.)
YEAR – third
MENTORS - Dr . GS Javed ( Technical Lead @ intel )
- Prof . Naushad Alam ( Department of Electronics Engg. ,AMU)
- Prof . Atiqur Rahman ( Department of Electronics Engg. ,AMU)

## Slide 2: INTERNSHIP OBJECTIVES
Design and Simulation of CS Amplifier ( NMOS + Current Source )
Design and Simulation of Common Drain Amplifier
Design of Simple Current Mirror
CS Amplifier for Design of Differential Pair
Design and Simulation of Differential Pair
Design and Simulation of Single Stage OPAMP
Design and Simulation of Two Stage OPAMP
SOFTWARE USED : LT Spice , ADT (Analog Designer Toolbox)
TECHNOLOGY NODE : 180n
DESIGN METHODOLOGY : Gm over Id method

## Slide 3: INTERNSHIP OVERVIEW
Week 1 to week 5

## Slide 4: WEEK 1 INTERNSHIP OVERVIEW
Gained proficiency in LTspice for circuit analysis and design.
Used LTspice and MS Excel to plot parameter charts using
Gm over Id methodology.
Designed a Common Source Amplifier using the Gm over Id method.
Initial Design Constraints: No specific constraints, focused on understanding the design process.
New Design Constraint: Optimizing the W/L ratio for improved performance based on feedback

## Slide 5: WEEK 2 INTERNSHIP OVERVIEW
Design constraint: Optimized W/L ratio in circuit design.
Designed Common Source Amplifier, Common Drain Amplifier
Simple Current Mirror, and Differential Pair using the Gm over Id
method.
Additional Design constraint: Designing circuits using unit devices.

## Slide 6: WEEK 3 INTERNSHIP OVERVIEW
Design constraint: Optimized W/L ratio and using unit devices in circuit design
Designed Common Source Amplifier, Differential Pair, and Single-Stage Op Amp with GBW = 1GHz.
Designed a Two-Stage Op Amp with a gain > 60dB using the Gm over Id method

## Slide 7: WEEK 4, 5
INTERNSHIP WORK

## Slide 8
For designing circuits , NMOS AND PMOS parameter charts are required .
Here , ADT is used to generate the Parameter Charts for NMOS and PMOS for 180nm Technology

## Slide 10: COMMON SOURCE AMPLIFIER using Gm over Id Method
Using nMOS AND CURRENT SOURCE LOAD
Model file : 180n
SPECIFICATIONS
GBW=1GHz , Gain =10 at 100MHz

## Slide 11
CALCULATIONS
GBW=1GHz , Gain =10 at 100MHz
Let = 2mS (Assumed ) CL= = 0.27pF
Taking Id = = 166.67uA = 167uA
For NMOS : (From Look Up Tables in ADT)
For , , , Vgs=0.6238
Hence , Gds= = 23.892uS W= =17.84.u (Taken 17.82u)
For PMOS : (From Look Up Tables in ADT)
From Id vs Gm/Id graph , AT Id=167uA , Gm/Id=8.989 Hence , Gm=1.5mS
For , , , Vsg=0.6798
Hence , Gds= = 23.9uS W= =34.784u (Taken 34.74u)
And , Vb = 1.8 – 0.6798 = 1.1202 Rout = 20.924K

## Slide 12
SCHEMATIC IN LT SPICE

## Slide 13
SPICE ERROR LOG & TRANSFER FUNCTION

## Slide 14
TRANSIENT ANALYSIS
Gain =10 at 100MHz , Input given is 10mV

## Slide 15
AC ANALYSIS
GBW=1.04 GHz
Gain ( In Decibel )
Frequency

## Slide 16
AC ANALYSIS
Gain 10.07 at 100MHz
Gain ( In Volts/Volts )
Frequency

## Slide 17
SPECIFICATION | SIMULATION RESULTS
At 100MHz , Gain=10 | At 100MHz , Gain=10.07
GBW=1GHz | GBW=1.04GHz
SUMMARY OF DESIGN OF CS AMPLIFIER

## Slide 18: COMMON SOURCE AMPLIFIER for Design of Differential Pair
Using nMOS AND CURRENT SOURCE LOAD
Model file : 180n
SPECIFICATIONS
GBW=1GHz , Gain =10 at 100MHz

## Slide 19
CALCULATIONS
GBW=1GHz , Gain =10 at 100MHz
Let = 2mS (Assumed ) CL= = 0.29pF
Taking Id = = 166.67uA = 167uA
For NMOS : (From Look Up Tables in ADT)
For , , Vgs=0.7417 hence Vg =1.1917
Hence , W= =16.84u (Taken 16.92u)
For PMOS : (From Look Up Tables in ADT)
From Id vs Gm/Id graph , AT Id=167uA , Gm/Id=4.144 Hence , Gm=0.69mS
For , , Vsg=0.8743
Hence , W= =10u (Taken 9.9u)
And , Vb = 1.8 – 0.8743= 0.9257

## Slide 20
SCHEMATIC IN LT SPICE

## Slide 21
SPICE ERROR LOG & TRANSFER FUNCTION

## Slide 22
TRANSIENT ANALYSIS
Gain =10 at 100MHz , Input given is 10mV

## Slide 23
AC ANALYSIS
GBW=1.04 GHz
Gain ( In Decibel )
Frequency
GBW=1.038 GHz

## Slide 24
AC ANALYSIS
Gain 10.07 at 100MHz
Gain ( In Volts/Volts )
Frequency
Gain 10.00498 at 100MHz

## Slide 25
SPECIFICATION | SIMULATION RESULTS
At 100MHz , Gain=10 | At 100MHz , Gain=10.004
GBW=1GHz | GBW=1.038GHz
SUMMARY OF DESIGN OF CS AMPLIFIER For Designing Differential Pair

## Slide 26: DIFFERENTIAL PAIR DESIGN ( Gm over Id Method )
DESIGN AND SIMULATION using lt spice
Model file : 180n
SPECIFICATIONS
GBW= 1GHz
Gain = 10 at 100 MHz frequency

## Slide 27
DIFFERENTIAL PAIR SCHEMATIC IN LT SPICE

## Slide 28
SPICE ERROR LOG & TRANSFER FUNCTION

## Slide 29
TRANSIENT ANALYSIS
Gain =10 at 100MHz , Input given is 10mV

## Slide 30
AC ANALYSIS
GBW=1.04 GHz
Gain ( In Decibel )
Frequency
GBW=1.038 GHz
GBW=1.038 GHz

## Slide 31
AC ANALYSIS
Gain 10.07 at 100MHz
Gain ( In Volts/Volts )
Frequency
Gain 10.00498 at 100MHz
Gain 10.043 at 100MHz
Gain 10.043 at 100MHz

## Slide 32
SPECIFICATION | SIMULATION RESULTS
At 100MHz , Gain=10 | At 100MHz , Gain=10.04
GBW=1GHz | GBW=1.038GHz
SUMMARY OF DESIGN OF DIFFERENTIAL PAIR

## Slide 33: SINGLE SATGE OPAMP DESIGN (Gm over Id Method)
DESIGN AND SIMULATION using lt spice
Model file : 180n
SPECIFICATIONS
GBW= 1GHz
Gain = 10 at 100 MHz frequency

## Slide 34
SINGLE STAGE OPAMP SCHEMATIC IN LT SPICE

## Slide 35
SPICE ERROR LOG & TRANSFER FUNCTION

## Slide 36
TRANSIENT ANALYSIS
Gain =10 at 100MHz , Input given is 10mV

## Slide 37
AC ANALYSIS
GBW=1.04 GHz
Gain ( In Decibel )
Frequency
GBW=1.038 GHz
GBW=1.038 GHz
GBW=955MHz
GBW=955MHz

## Slide 38
AC ANALYSIS
Gain 10.07 at 100MHz
Gain ( In Volts/Volts )
Frequency
Gain 10.00498 at 100MHz
Gain 10.043 at 100MHz
Gain 10.043 at 100MHz
Gain 10.149 at 100MHz

## Slide 39
SPECIFICATION | SIMULATION RESULTS
At 100MHz , Gain=10 | At 100MHz , Gain=10.14
GBW=1GHz | GBW=955MHz
SUMMARY OF DESIGN OF SINGLE STAGE OPAMP

## Slide 40: DESIGN OF TWO SATGE OPAMP (Gm over Id Method )
DESIGN AND SIMULATION using lt spice
Model file : 180n
SPECIFICATIONS
Gain > 60dB
CONSTRAINTS = (CL=20f , Phase Margin >50 Degree)

## Slide 41
CALCULATIONS for FIRST STAGE
Gain = 40 , =20f , Rout = 93 KΩ (Assumed after Back Calculations)
Let = = 0.43mS
Taking Id = = 35.83uA
For NMOS : (From Look Up Tables in ADT)
For , 77.05 , , Vgs=0.7316
Hence , Gds= = 5.58uS W= =3.6u and Vg =0.7316+0.45
Vg = 1.18
For PMOS :
As , Rout = Ro(NMOS) || Ro(PMOS) Gds(PMOS)= - Gds(NMOS)
Hence , Gds(PMOS)= 5.172uS
Now , as current will remain same i.e 35.83uA
=6.93 using this From LUT in ADT , Gm/Id is calculated for PMOS

## Slide 42
Hence , Gm (PMOS) = 5.487 * 35.83uA = 0.196mS
For Vsg=0.781
Hence , W= = 3.317 (Taken 3.24u)
And Vb = 1.8 – 0.781 = 1.019
AS CL=20f BW (-3dB) = 85.56MHz

## Slide 43
SCHEMATIC IN LT SPICE

## Slide 44
CALCULATIONS for Next STAGE
( COMMON SOURCE USING PMOS AND CURRENT SOURCE LOAD )
Gain = 28 , =20f
For PMOS :
Taking = 8 * 0.43mS = 3.44 mS
As Av=Gm*Rout Rout = Av/Gm=8.139K
Vb(PMOS) = 1.0296 V Vsg=0.7704
From ADT , For Vsg =0.7704 Gm/Id is Calculated Id=607.8U
Now , for above Gm/Id ,
Hence , Gds = 71.7uS W = 57.84u
For NMOS :
As , Rout = Ro(NMOS) || Ro(PMOS) Gds(NMOS)= - Gds(PMOS)

## Slide 45
Hence , Gds(NMOS)= 48.5uS
Now , as current will remain same i.e 607.98uA
=12.534 using this From LUT in ADT ,
Gm/Id is calculated for NMOS
Hence , Gm (PMOS) = 5.61 * 607.98uA = 3.41mS
For Vgs=0.7913
Hence , W= 16.56u

## Slide 46
SCHEMATIC IN LT SPICE

## Slide 47
TWO STAGE OPMAP SCHEMATIC IN LT SPICE
47 degree

## Slide 48
SPICE ERROR LOG AND TRANSFER FUNCTION

## Slide 49
TRANSIENT ANALYSIS
Gain > 1000 at 10k , Input given is 1uV

## Slide 50
AC ANALYSIS
GBW=1.04 GHz
Gain ( In Decibel )
Frequency
GBW=1.038 GHz
GBW=1.038 GHz
GBW=955MHz
GBW=955MHz
GBW=1.01GHz
Gain Margin=47°

## Slide 51
SPECIFICATION | SIMULATION RESULTS
Gain>1000 i.e. 60dB | Gain=1125 i.e. 61.03dB
GBW=1GHz | GBW=1.01GHz
Phase Margin > 50° | Phase Margin = 47°
SUMMARY OF DESIGN OF SINGLE STAGE OPAMP

## Slide 52
SUMMARY
Designed and Simulated Various Circuits using Gm over Id Method such as :
Common Source , Common Drain Amplifier , Current Mirror , CS Amplifier for Differential Pair Design , Differential Pair , Single Stage Op Amp , and Two Stage Op Amp
Software Used: LTspice, Analog Designer Toolbox (ADT)
Final Project: Design and Simulation of Two Stage Op Amp with Gain > 1000 (60 dB)
Results: All simulation results met the specifications.

## Slide 53
SPECIAL THANKS TO :
Dr. Saif Abrar Sir
Prof . Mohammad Jawaid Siddiqui Sir
Mudassir Sir
Shamshul Haq Sir
Mohd Kashif Sir
And My Internship Partners
Munazir Reza
Ayush Sharma
Mohsin Husain
&
My Parents
THANK YOU !