## Slide 1: DESIGN OF COMMON SOURCE AMPLIFIER (REDESIGNED)
As w/l ratio was very high in previous design approach and simulations result were not exactly matching the specification

## Slide 2: COMMON SOURCE AMPLIFIER
Using NMOS AND PASSIVE LOAD
Model file : 180n
SPECIFICATIONS
GBW=800MHz , VDD=1.8V , L=0.36u

## Slide 3
CALCULATIONS
GBW=800MHz , L=0.36u , Vdd=1.8V, Model file = 180n
Let GAIN (A) = 10
f(-3db) = = 80MHz LET Gm=2mS (Practical value range 1-3 S given by Javed Sir)
USING = =0.397pF (assume 0.3pF)
Now by Back calculation ,
= =1.5mS
Assume Vov=0.2V Vgs=0.65V Id= =150uA
Then , Gm/Id = 10
R=(1.8 – 0.9)/150uA=6 Kohm
W is calculated by sweeping for 150uA current

## Slide 4
SCHEMATIC IN LT SPICE

## Slide 6
TRANSIENT ANALYSIS IN LT SPICE

## Slide 7
FREQUENCY RESPONSE IN LT SPICE

## Slide 8: COMMON SOURCE AMPLIFIER
Using PMOS AND PASSIVE LOAD
Model file : 180n
SPECIFICATIONS
GBW=800MHz , VDD=1.8V , L=0.36u

## Slide 9
CALCULATIONS
GBW=800MHz , L=0.36u , Vdd=1.8V, Model file = 180n
LET Gm=3mS (Practical value range 1-3 S given by Javed Sir)
USING = =0.49pF (assume 0.5pF)
Now by Back calculation ,
= =2.5mS
Assume Vov=0.2V Vg=1.1V Id= =312uA
Then , Gm/Id = 8.01
R=(1.8 – 0.9)/312uA= 2.88 Kohm
W is calculated by sweeping for 312uA current

## Slide 10
SCHEMATIC IN LT SPICE

## Slide 12
TRANSIENT ANALYSIS IN LT SPICE

## Slide 13: COMMON SOURCE AMPLIFIER
Using NMOS AND CURRENT SOURCE LOAD
Model file : 180n
SPECIFICATIONS
GBW=1GHz , Gain = 10 at 100MHz

## Slide 14
CALCULATIONS
GBW=1GHz , Gain = 10 at 100MHz
LET Gm=2mS (Practical value range 1-3 S given by Javed Sir)
USING = =0.318pF (assume 0.3pF)
Now by Back calculation ,
= =1.884mS
(For nmos) Vov=0.2V Vgs=0.65V Id= = 188uA
Then , Gm/Id = 10.021 Id/W = 13.6
W=14u
(For pmos) Vg=1.1V
Width of PMOS is taken twice as that of nmos
W=28u
NOTE : Now some manipulations are done in calculations to meet the specifications

## Slide 15
SCHEMATIC IN LT SPICE

## Slide 17
TRANSIENT ANALYSIS IN LT SPICE

## Slide 18
FREQUENCY RESPONSE IN LT SPICE

## Slide 20
THANK YOU