## Slide 1: WEEK 1
Internship under dr gs javed sir
INTERN NAME - AFZAL MALIK
College/UNIVERSITY – ZAKIR HUSAIN COLLEGE OF ENGG. & TECH.
ALIGARH MUSLIM UNIVERSITY
COURSE- BACHELOR OF TECHNOLOGY (ELECTRONICS ENGG.)
YEAR – SECOND

## Slide 2: WEEK 1 INTERNSHIP PLAN
To be able to perform .dc /.op / .tran Simulations
To design Common Source and Common Drain Amplifier ( Used Gm over Id Method )
SOFTWARE USED : LT Spice , MS Excel

## Slide 3: BASIC CIRCUIT SIMULATIONS
.Dc , .op and .tran Simulation of basic circuits using lt spice

## Slide 4: DESIGN OF COMMON SOURCE AMPLIFIER ( USING GM OVER ID METHOD )

## Slide 5: PARAMETER CHARTS
IN ORDER TO DESIGN AN AMPLIFIER USING GM OVER ID METHODOLOGY WE REQUIRE PARAMETER CHARTS :
a) Primary Charts
Gm/Gds vs Gm/Id
Id/W vs Gm/Id
Ft vs Gm/Id
b) Secondary Charts
1)Cgd/Cgg vs Gm/Id
2)Cdd/Cgg vs Gm/Id

## Slide 6: Plotting Parameter Charts
Using lt spice and ms excel
Model file : 180n

## Slide 7: LT SPICE SETUP TO PLOT CHARTS FOR NMOS

## Slide 8
AFTER MAKING THE SETUP IN LT SPICE
Id vs Vgs is plotted by sweeping vgs from 0 to 1.8 V
Gm [ d(Id(M1)] vs Vgs is plotted by sweeping vgs from 0 to 1.8 V
Id vs Vds is plotted by sweeping vds from 0 to 1.8 V
Gds [ d(Id(M1)] vs Vds is plotted by sweeping vgs from 0 to 1.8 V
All this data is transferred in MS Excel and then
Gm/Gds vs Gm/Id is plotted
Id/W vs Gm/Id is plotted
Hence , we got two of the parameter charts that are required to design Common Source Amplifier

## Slide 9
Chart: PLOT OF Gm/Gds vs Gm/Id

## Slide 10
Chart: PLOT OF Id/W vs Gm/Id

## Slide 11: LT SPICE SETUP TO PLOT CHARTS FOR PMOS

## Slide 12
Chart: Gm/Gds vs Gm/Id

## Slide 13
Chart: PLOT OF Id/W vs Gm/Id

## Slide 14: COMMON SOURCE AMPLIFIER
Using NMOS AND PASSIVE LOAD
Model file : 180n
SPECIFICATIONS
GBW=800MHz , VDD=1.8V , L=0.36u

## Slide 15
CALCULATIONS
GBW=800MHz , L=0.36u , Vdd=1.8V, Model file = 180n
Let GAIN (A) = 10
f(-3db) = = 80MHz let CL=5pF
USING f(-3db) = Rout = 397.88 ohm
Now , Gain (A) = Gm Rout Gm=25.1 mS
Now , Let Gm/Id = 10.2 Id = 2.46 mA
(From NMOS Parameter Charts)
Gm/Gds = 69.9 Gds=359 uS
AS Ro=1/Gds , Ro=2785 ohm
(From NMOS Parameter Charts)
Id/W= 13.6 W=180u

## Slide 16
CALCULATIONS
Now Rout = Ro || RL RL =
RL = 464.197 ohms
Now, Vgs is calculated from Gm/Id vs Vgs Curve in LT Spice
For , Gm/Id = 10.2
Vgs = 702mV = 0.702V

## Slide 17
SCHEMATIC IN LT SPICE

## Slide 18
.OP ANALYSIS IN LT SPICE

## Slide 20
TRANSIENT ANALYSIS IN LT SPICE

## Slide 21
FREQUENCY RESPONSE IN LT SPICE

## Slide 22
SIMULATIONS RESULT
GBW=837MHz
Gain= 10.2737

## Slide 23: COMMON SOURCE AMPLIFIER
Using PMOS AND PASSIVE LOAD
Model file : 180n
SPECIFICATIONS
GBW=800MHz , VDD=1.8V , L=0.36u

## Slide 24
CALCULATIONS
GBW=800MHz , L=0.36u , Vs=1.8V, Model file = 180n
Let GAIN (A) = 10
f(-3db) = = 80MHz let CL=5pF
USING f(-3db) = Rout = 397.88 ohm
Now , GAIN (A) = Gm Rout Gm=25.1 mS
Now , Let Gm/Id = 10.2 Id = 2.46 mA
(From NMOS Parameter Charts)
Gm/Gds = 72.2 Gds=347.64 uS
AS Ro=1/Gds , Ro=2876.5 ohm
(From NMOS Parameter Charts)
Id/W= 3.3 W=745u

## Slide 25
CALCULATIONS
Now Rout = Ro || RL RL =
RL = 461.75 ohms
Now, Vgs is calculated from Gm/Id vs Vgs Curve in LT Spice
For , Gm/Id = 10.2
Vg = 1.1V

## Slide 26
SCHEMATIC IN LT SPICE

## Slide 29
TRANSIENT ANALYSIS IN LT SPICE

## Slide 30
FREQUENCY RESPONSE IN LT SPICE

## Slide 31
SIMULATIONS RESULT
GBW=763MHz
Gain= 10.756

## Slide 32: COMMON DRAIN AMPLIFIER (SOURCE FOLLOWER)
Using NMOS AND RESITANCE
Model file : 180n
SPECIFICATIONS
VDD=1.8V , L=0.36u , GAIN(A)=0.95
Rout=50 ohm, CL = 5pf

## Slide 33
CALCULATIONS
VDD=1.8V , L=0.36u , GAIN(A)=0.95
Rout=50 ohm, CL = 5pf
Using B.W = BW= 636.61MHz
Now , Gain (A) = and Rout = 1/Gm||Ro||Rs
On solving both the equation , we get
Gm=19mS =1000 ohm
Now , let Gm/Id = 15.1 Id=1.26mA
Gm/Gds = 38.2 Gds=497uS Ro=2.012 K ohm
And hence , Rs=1.988 K ohm ( by further inspection taken as 720 ohm )
Vgs = 0.543V Vg = vgs + vs =1.443 V
Id/W=5.65 W=223u

## Slide 34
SCHEMATIC IN LT SPICE

## Slide 36
TRANSIENT ANALYSIS IN LT SPICE

## Slide 37
FREQUENCY RESPONSE IN LT SPICE

## Slide 38
Feedback I got
Specifications are not exactly matching with simulations , W/L ratio is very high , so now I have to redesign them by making slight modification in design approach

## Slide 39
THANK YOU